## Slide 1: Packet Data Convergence Protocol (PDCP) specification
3GPP TS 38.323 version 18.5.0 Release 18

## Slide 2: Packet Data Convergence Protocol (PDCP)
It is configured by upper layers, such as RRC.
The PDCP sublayer is used for Radio Bearers (RBs) mapped on DCCH, DTCH, MTCH, SCCH, and STCH logical channels.
Generally, each RB is associated with one PDCP entity.

## Slide 3: Key functions supported by PDCP
Transfer of data, for both user plane and control plane.
Maintenance of PDCP Sequence Numbers (SNs).
Header compression and decompression, supporting protocols like ROHC, EHC, and UDC.
Ciphering and deciphering for data security.
Integrity protection and integrity verification.
Timer-based SDU discard.
Reordering and in-order delivery of data packets.
Duplicate discarding.

## Slide 4: Key services supported by PDCP to RRC or SDAP
Transfer of user plane data.
Transfer of control plane data.
Header compression.
Uplink data compression.
Ciphering.
Integrity protection.

## Slide 5: Medium Access Control (MAC) protocol specification
3GPP TS 38.321 version 18.5.0 Release 18

## Slide 6: Medium Access Control (MAC) protocol specification
The NR Medium Access Control (MAC) protocol specification describes the functionality of the MAC sublayer. The MAC entity is configured by RRC and handles various transport channels, including Broadcast Channel (BCH), Downlink Shared Channel(s) (DL-SCH), Paging Channel (PCH), Uplink Shared Channel(s) (UL-SCH), Random Access Channel(s) (RACH), Sidelink Broadcast Channel (SL-BCH), and Sidelink Shared Channel (SL-SCH). Multiple MAC entities can be configured, for example, when Secondary Cell Group (SCG) or Dual Active Protocol Stack (DAPS) handover is used. The MAC entity is responsible for mapping logical channels onto transport channels.

## Slide 7: Functions provided by MAC
Mapping between logical channels and transport channels.
Multiplexing and demultiplexing of MAC SDUs onto and from transport blocks.
Error correction through HARQ (Hybrid Automatic Repeat reQuest).
Logical channel prioritization.
Scheduling information reporting.
Priority handling between overlapping resources of one UE.
Radio resource selection.

## Slide 8: Services Provided by MAC to Upper Layers
Data transfer
Radio resource allocation

## Slide 9: Radio Link Control (RLC) protocol specification
3GPP TS 38.322 version 18.2.0 Release 18

## Slide 10: Radio Link Control (RLC)
Radio Link Control (RLC) sublayer is specified for the NR radio interface and is configured by upper layers, such as RRC. It sits between upper layers (like PDCP) and lower layers (like MAC). RLC functionality is performed by RLC entities, which can be configured to operate in one of three modes: Transparent Mode (TM), Unacknowledged Mode (UM), or Acknowledged Mode (AM). An RLC entity receives/delivers RLC SDUs from/to upper layers and sends/receives RLC PDUs to/from its peer entity via lower layers.

## Slide 11: RLC sublayer supports key functions:
Transfer of upper layer PDUs (RLC SDUs).
Error correction* through ARQ, which is exclusively for AM data transfer.
Segmentation and reassembly of RLC SDUs, used for UM and AM data transfer.
Re-segmentation of RLC SDU segments, performed only in AM.
Duplicate detection, also specific to AM data transfer.
RLC SDU discard, applicable to UM and AM data transfer.
RLC re-establishment.
Protocol error detection, only for AM data transfer.

## Slide 12: RLC supports services to upper layers:
TM data transfer.
UM data transfer.
AM data transfer, including indication of successful delivery of upper layer PDUs.
RLC expects services from lower layers, such as data transfer and notification of transmission opportunities, typically from MAC.

## Slide 13: Radio Resource Control (RRC); Protocol specification
3GPP TS 38.331 version 18.5.1 Release 18

## Slide 14: Radio Resource Control (RRC)
Radio Resource Control (RRC) protocol specification defines the functionality of the RRC sublayer in 5G NR.
RRC operates in the control plane of the Access Stratum (AS).

## Slide 15: Key functions of the RRC layer include
Broadcast of system information (e.g., cell (re-)selection parameters, common channel configuration, ETWS/CMAS notifications, positioning assistance data).
RRC connection control, which involves procedures for establishment, modification, suspension, resumption, and release of the RRC connection.
AS security activation, configuring integrity protection and ciphering for SRBs and DRBs.
Radio Bearer configuration, managing the establishment, modification, suspension, resumption, and release of SRBs, DRBs, and MRBs.
RRC connection mobility*, handling intra-frequency and inter-frequency handover, and path switch.

## Slide 16: Key functions of the RRC layer include
Measurement configuration and reporting (setting up measurement objects, reporting configurations, and measurement gaps).
Recovery from radio link failure.
Inter-RAT mobility.
Configuration for IAB-nodes, L2 U2N/U2U relay, and NCR-nodes.

## Slide 17: RRC provides services to upper layers
Broadcast of common control information.
Notification of UEs (e.g., paging for RRC\_IDLE/INACTIVE UEs).
Transfer of dedicated signaling.
Broadcast of positioning assistance data.
Transfer of application layer measurement configuration and reporting
RRC expects services from lower layers, primarily *integrity protection, ciphering, and loss-less in-sequence data delivery without duplication..