## Slide 1
A Conformance and Performance Analysis Based on 3GPP TS 38.322
DESIGN AND VERIFICATION OF RLC AM AND UM MODES IN 5G NR

## Slide 2
PROJECT OBJECTIVE & SCOPE
TO DESIGN AND EXECUTE TEST SCENARIOS TO VERIFY THE PERFORMANCE OF THE 5G RLC LAYER AGAINST THE 3GPP STANDARD.
  Simulate RLC PDU handling as defined in Section 6.2 of TS 38.322.
  Measure Key Performance Indicators (KPIs) like Throughput, Latency, and Retransmission Rate.
  Analyze the behavior of RLC's primary data transfer modes.
  This project focuses on Acknowledged Mode (AM) and Unacknowledged Mode (UM), the two most critical modes for user data transfer.
Core Tasks
Scope
01
02

## Slide 3
WHY TEST RLC?
THE IMPORTANCE OF RELIABLE DATA DELIVERY
The air interface is inherently unreliable. The RLC layer is designed to fix this.
We ensure the implementation correctly provides the "services to upper layers" described in Section 4.3 of the standard.
The 5G Challenge:
Why We Test:

## Slide 4
RLC MODES: AM
VS UM
INTRODUCING THE RLC MODES
  Description: Provides reliable, in-order delivery using a feedback-based error correction mechanism.
  Standard Reference: Defined in Section 4.2.1.3 of TS 38.322.
  Use Case: HTTP (Web), FTP (Files), applications requiring guaranteed data integrity.
  Description: Provides low-latency, in-order delivery but does not guarantee against loss.
  Standard Reference: Defined in Section 4.2.1.2 of TS 38.322.
  Use Case: VoIP, Live Video Streaming, applications where timeliness is more critical than 100% reliability.
Acknowledged Mode (AM)
Unacknowledged Mode (UM)
01
02

## Slide 5
UNACKNOWLEDGED MODE : THE "SPEED FIRST" APPROACH
  Core Principle: Prioritize low latency by eliminating the delay of feedback and retransmissions.
  PDU Structure (TS 38.322, Sec 6.2.2.3):
    An UMD PDU consists of a header and a data field.
    The header is simple, containing a Sequence Number (SN) and Segmentation Info (SI).
    The SN can be 6 or 12 bits, configured by RRC, defining the window size for reordering.
    The 2-bit SI field indicates if the PDU contains a full SDU, a first segment, a last segment, or a middle segment.
  Key Limitation: As per the standard, there is no mechanism for the receiver to request retransmission of a lost UMD PDU.

## Slide 6
HOW UM WORKS: SEGMENTATION & REASSEMBLY
  Segmentation (Sender Side):
    When an SDU arrives, the sender checks if it fits in a single PDU.
    If not, it segments the SDU. It creates the first PDU with SI = '01' (first segment), middle PDUs with SI = '11', and the final PDU with SI = '10' (last segment). Each segmented PDU gets the same SN.
  Reassembly (Receiver Side - TS 38.322, Sec 5.2.2.2):
    The receiver uses the SN to reorder incoming PDUs.
    The t-Reassembly timer is crucial. If the receiver has some segments of an SDU but not all, it starts this timer.
    If the timer expires before the missing segments arrive, the receiver must discard all received segments of that SDU. This is the defined behavior for handling data loss in UM.

## Slide 7
HOW UM WORKS: SEGMENTATION & REASSEMBLY

## Slide 9
ACKNOWLEDGED MODE (AM): THE "RELIABILITY FIRST" APPROACH
  Core Principle: Achieve error-free delivery through a closed-loop feedback system.
  PDU Structure (TS 38.322, Sec 6.2.2.4):
  An AMD PDU header is more complex. It contains a D/C (Data/Control) bit, a P (Poll) bit, SI, and a longer SN (12 or 18 bits).
  The longer SN supports a much larger transmission window, essential for high-speed 5G links.
  Key Mechanism: ARQ (Automatic Repeat reQuest), a protocol built on a constant dialogue between the sender and receiver

## Slide 10
HOW AM WORKS: THE ARQ FEEDBACK LOOP
  1. Status Reporting (Receiver's Feedback):
    The receiver sends a STATUS PDU (identified by D/C bit = '0').
    This PDU contains an ACK_SN to confirm reception up to a point, and one or more NACK_SN fields to report specific gaps.
    It can even report partial gaps using SOstart / SOend fields for maximum efficiency.
  2. Polling (Sender's Request for Feedback - Sec 5.3.3):
    The sender sets the P-bit to '1' in an AMD PDU header to request a status report.
    This is triggered by configurable parameters like pollPDU (number of PDUs sent) or pollByte (volume of data sent).
  3. Retransmission (Sender's Corrective Action - Sec 5.3.2):
    Upon receiving a STATUS PDU, the sender inspects the NACKs.
    It retrieves the missing data from its buffer and schedules it for retransmission, prioritizing it over new data.
    The RETX_COUNT for that SDU is incremented. If it reaches maxRetx Threshold, the SDU is discarded and upper layers are notified.

## Slide 13
THE ARQ CONVERSATION: KEY TIMERS
  t-Poll Retransmit (Sender Side): This is the sender's watchdog timer. When a poll is sent, this timer starts. If it expires before a STATUS PDU is received, the sender assumes the report was lost and initiates a new poll/retransmission. This prevents deadlocks.
  t-Reassembly (Receiver Side): The receiver's patience timer. If it has an incomplete SDU and waits too long for the missing pieces, this timer expires, triggering it to send a STATUS PDU to complain about the gaps.
  t-Status Prohibit (Receiver Side): Prevents the receiver from spamming STATUS PDUs. After sending one, it cannot send another until this timer expires, even if new errors are detected. This reduces control plane overhead.

## Slide 14
Set up the RLC entity in either AM or UM mode, with parameters like SN size, window size, and timer values.
Feed a stream of SDUs into the RLC sender.
Pass the resulting PDUs through a channel with pre-defined, repeatable packet loss patterns.
Configure
Inject
Simulate
TEST SETUP & METHODOLOGY
Capture detailed logs of PDU transmission/reception, timer starts/stops, and buffer states.
Process logs to calculate KPIs and compare behavior against the standard.
Monitor & Log
Analyze

## Slide 15
KEY PERFORMANCE INDICATORS (KPIS) TO MEASURE
The time from when an SDU is passed to the RLC sender until it is successfully delivered by the RLC receiver.
The percentage of SDUs that were discarded by the RLC layer (either due to maxRetxThreshold in AM or reassembly failure in UM).
The ratio of retransmitted PDUs to total transmitted PDUs.
Latency (ms)
Application Packet Loss Rate (%)
RLC Retransmission Rate (%)
01
02
03

## Slide 16
UNACKNOWLEDGED MODE (UM) TEST SCENARIOS & RESULTS

## Slide 17
ACKNOWLEDGED MODE (AM) TEST SCENARIOS & RESULTS

## Slide 18
CONCLUSION & FUTURE WORK
  Conclusion: This project successfully designed a test framework and used it to verify the functionality and quantify the performance of RLC AM and UM modes. The results demonstrate that the implementation conforms to the 3GPP standard and performs as expected.
  Future Work:
    Handover Testing: Test RLC re-establishment procedures (Section 5.1.2), which are critical for mobility.
    Parameter Tuning: Analyze the performance impact of changing configurable parameters like t-PollRetransmit and maxRetxThreshold.
    Advanced Scenarios: Introduce scenarios with sidelink communication (V2X) or for MBS (Multicast Broadcast Services), which also use RLC.