## Slide 1: 5G Core Network: Service-Based Architecture (SBA)
Network Function Mapping & Interface Design
Presented by: Abhijith Sai Vedantham

## Slide 2: Fig: 5G Core Network: Service-Based Architecture (SBA)
gNB
(5G NR)
UPF
DN
(Data Network)
AMF
(Access and Mobility Management Function)
SMF
Session Management Function
PCF
Policy Control Function
NRF
Network Repository Function
NEF
Network Exposure Function
UDM
Unified Data Management
AUSF
Authentication Server Function
UDR
Unified Data Repository
NSSF
Network Slice Selection Function
SMSF
SMS Function
AF
External
Application
UE
Service-Based Interface (SBI) Bus
HTTP/2 = REST - JSON
N1
N6
N2
N3
N4
Refererence Point Architecture
Outside the bus: N1,N2,N3,N4,N6
Inside the bus: Npcf, Namf, Nnrf etc. service-based
Network Slicing Support
.NSSF manages slice selection
.Multiple instances of NFs can be deployed

## Slide 3: Introduction to 5G Core SBA:
5G Core uses a modern, flexible Service-Based Architecture (SBA).
Network Functions (NFs) behave as independent services.
Communication occurs over HTTP/2 protocols with RESTful APIs.
Designed for cloud-native, scalable, and modular deployments.
Enables dynamic function updates and service discovery.

## Slide 4: Key Network Functions in 5G Core:
Key Network Functions in 5G Core AMF (Access and Mobility Management Function):Handles device registration, connection management, mobility (handover)
SMF (Session Management Function):Manages PDU sessions, IP allocation, and session control policies
UPF (User Plane Function):Routes and forwards user data packets between UE and data networks
PCF (Policy Control Function):Defines QoS and enforces network policies for sessions

## Slide 5: Key Network Functions in 5G Core:
AUSF (Authentication Server Function):Authenticates user credentials during connection setup
NRF (Network Repository Function):Maintains an NF directory for discovery and registration
NSSF (Network Slice Selection Function):Determines and allocates appropriate network slices for users
NEF (Network Exposure Function):Provides API interfaces to third-party and application functions

## Slide 6: Key Network Functions in 5G Core:
SMSF (SMS Function):Manages SMS delivery over the 5G core
UDR (Unified Data Repository):Central database shared by multiple functions like UDM and PCF
UDM (Unified Data Management):Stores user profiles, subscription info, authentication credentials
AF (Application Function):Application logic that interacts with 5G core via NEF

## Slide 7: Service-Based Interfaces (SBIs) Explained:
SBIs enable NFs to communicate with each other via standardized APIs.
Uses RESTful API calls over HTTP/2 protocol with JSON data exchange.
Important SBI examples include:

## Slide 8: Service-Based Interfaces (SBIs) Explained:
Nnrf: NF discovery and registration with NRF
Namf: UE registration and mobility messaging between UE and AMF
Nsmf: Session control messaging between AMF and SMF
Npcf: Policy control communication between SMF/AMF and PCF
Nudm: Access subscriber data via UDM

## Slide 9: Service-Based Interfaces (SBIs) Explained:
Nausf: User authentication processes via AUSF
Nnssf: Requests for network slice selection from NSSF
Nnef: Communication channel for AF to interact with NEF

## Slide 10: Interfaces Using HTTP/2 and JSON in 5G Core:
All 5G Core Service-Based Interfaces (SBIs) use:
HTTP/2 protocol for efficient transport
JSON format for data payload
RESTful API structure based on OpenAPI specs

## Slide 11: Interfaces Using HTTP/2 and JSON in 5G Core:
Key Interfaces Using HTTP/2 + JSON:
Nnrf: For NF discovery via NRF
Namf: UE access, registration, and mobility via AMF
Nsmf: Session and PDU control between AMF and SMF
Npcf: Policy exchange between SMF/AMF and PCF
Nudm: Access user profile data from UDM
Nausf: Perform authentication via AUS

## Slide 12: Interfaces Using HTTP/2 and JSON in 5G Core:
Key Interfaces Using HTTP/2 + JSON:
Nnssf: Slice selection queries to NSSF
Nnef: API interaction between AF and NEF
Nsmsf: SMS delivery using SMSF (if REST-based)
)

## Slide 13: FUNCTIONS of Core NFs:
AMF: Like a traffic controller managing device entry and movement
SMF: Session supervisor assigning IPs and managing data flows
UPF: The data router sending user traffic to the internet or apps
PCF: The policy manager defining speed limits and priorities

## Slide 14: FUNCTIONS of Core NFs:
NRF: The “yellow pages” for network functions to find each other
NSSF: The lane selector deciding the best network slice for each user

## Slide 15: UERANSIM and Open5GS Setup:
Setup:
UERANSIM simulates UE and gNB (for testing without hardware)
Open5GS is a free 5G core software that includes AMF, SMF, UPF, etc.
Used together to build and test full 5G core and RAN architecture

## Slide 16: UERANSIM and Open5GS Setup:
Requirments:
Linux system with MongoDB for NF database.
Configuration of PLMN, NSSAI, gNB ID in both UERANSIM and Open5GS.